## Slide 1: Overview
Introduction- Sequential Circuit
Flip-Flops & Latches SR latch
Types of flip-flop
Master-slave flip-flop
Registers
Counters
Shift Registers

## Slide 3: Introduction- Sequential Circuit
Fig.1. Block diagram of Sequential Circuits

## Slide 4: Sequential Circuit (contd…)
Outputs in a sequential circuit are a function not only of the inputs, but also of the present state of the storage elements.
Next state of the storage elements is also a function of external inputs and the present state.
Sequential circuit is specified by a time sequence of inputs, outputs, and internal states .
In contrast, the outputs of combinational logic depend only on the present values of the inputs.

## Slide 5: Sequential Circuit (contd…)
two types of sequential circuits - classification is a function of the timing of their signals
  Synchronous sequential circuit is a system whose behaviour can be defined from the knowledge of its signals at discrete instants of time.
  The behaviour of an asynchronous sequential circuit depends upon the input signals at any instant of time and the order in which the inputs change

## Slide 6: Synchronous clocked sequential circuit
Fig.2. Synchronous clocked sequential circuit

## Slide 7: Storage Elements: Latches
Storage elements that operate with signal levels (rather than signal transitions) –latches
Latches are said to be level sensitive devices
latches are the basic circuits from which all flip-flops are constructed
Not practical for use as storage elements in synchronous sequential circuits

## Slide 9: SR latch with NOR gates
SR latch constructed with two cross-coupled NOR gates
When output Q = 1 and Q’ = 0, the latch is said to be in the set state
When Q = 0 and Q’ = 1, , the latch is said to be in the reset state

## Slide 10
Latch
Operation
Figure 3: Characteristics of a SR Latch

## Slide 11
Latch
Operation contin..
Figure 4: Characteristics of a SR Latch
. . . . . . . . . . . . . . . . . . . .

## Slide 12: SR latch with NAND gates
In comparing the NAND with the NOR latch, note that the input signals for the NAND require the complement of those values used for the NOR latch.
Because the NAND latch requires a 0 signal to change its state, it is sometimes referred to as an S’R’ latch.

## Slide 13: SR latch with control input
It consists of the basic SR latch and two additional NAND gates.
The control input En acts as an enable signal for the other two inputs.
The outputs of the NAND gates stay at the logic-1 level as long as the enable signal remains at 0
When the enable input goes to 1, information from the S or R input is allowed to affect the latch
Indeterminate condition makes this circuit difficult to manage

## Slide 14: Clocks
Clocks
It controls the storage value.
It is a enable signal to decide when to take the new value of input and store in the latch.
Mostly, it is a square wave that goes either high to low or low to high.
Figure 6: Clock signal
Latches constructed using this clock signal are called as Flip-flops.
Types :
  SR flip flop
  D flip flop
  T flip flop
- JK flip flop