## Slide 1: 18ECC203J – Module 1 Intel 8086 – Architecture, Signals and Features S – 7 (2 of 2), 8, 11, 12
Prepared by,
Dr. R. Manohari
Dr.T.Rajalakshmi

## Slide 2: S – 7 (2 of 2) Methods of generating physical address in 8086 & Pin signals of 8086: Common signals
S – 8 Minimum mode signals & Maximum mode signals
S – 11 Minimum mode 8086 systems & Timings
S – 12 Maximum mode 8086 systems & Timings

## Slide 3: Pin Diagram of 8086 Microprocessor

## Slide 4: Two modes of 8086

## Slide 5: Common Signals in both modes

## Slide 6: AD0 – AD15 Pin 16-2, 39 (Bi-directional)
These lines constitute the time multiplexed memory/IO address & data bus.
It acts as address bus during the first part of machine cycle(T1) & data bus for the remaining part of the machine cycle

## Slide 7: A19/S6, A18/S5, A17/S4, A16/S3 Pin 35-38 (Unidirectional)
These are the time multiplexed address and status lines
During T1, they carry higher order 4-bit address.
In the remaining clock cycles, they carry status signals.

## Slide 8: Cont.
The status signals on S3 & S4 specifies the segment register used for calculating the physical address
The status line S5 indicates the status of an 8086 interrupt enable flag
The status line S6 is always low

## Slide 9: BHE / S7 Pin 34 (Output)
BHE stands for Bus High Enable.
BHE signal is used to indicate the transfer of data over higher order data bus (D15 – D8).
It is multiplexed with status pin S7.
S7 is not currently used

## Slide 10: Cont.

## Slide 11: RD (Read) Pin 32 (Output)
It is a read signal used for read operation.
RD is low whenever the 8086 is reading data from memory or an I/O device

## Slide 12: READY Pin 22 (Input)
This is an acknowledgement signal from slower I/O devices or memory.
When high, it indicates that the device is ready to transfer data.
When low, then microprocessor enters into wait state
This signal is used primarily to synchronize slower peripherals with the microprocessor

## Slide 13: RESET Pin 21 (Input)
It is a system reset.
It is an active high signal.
When high, microprocessor enters into reset state and terminates the current activity and start execution from FFFF0H.
It must be active for at least four clock cycles to reset the microprocessor.

## Slide 14: INTR Pin 18 (Input)
It is a level triggered maskable interrupt request.
It is sampled during the last clock cycle of each instruction to determine if the processor should enter into an interrupt service routine.

## Slide 15: NMI Pin 17 (Input)
It is a positive edge triggered non-maskable interrupt request.
It causs a Type 2 interrupt.

## Slide 16: TEST Pin 23 (Input)
If low, execution continues else microprocessor enters into wait state
This input is examined by the ‘WAIT’ instruction
This input is synchronized internally during each clock cycle on the leading edge of the clock cycle

## Slide 17: CLK Pin 19 (Input)
This clock input provides the basic timing for processor operation and bus control activity.
Clock frequency depends on the version of 8086
It requires clock signal ( with 33% duty cycle) from some external, crystal controlled generator to synchronize internal operations

## Slide 18: VCC & GND Pin 40, 1 & 20
VCC: +5 V power supply for the operation of the internal circuit
GND: ground for the internal circuit

## Slide 19: Two modes of 8086 Minimum Mode Signals

## Slide 20: Minimum Mode Signals
For this mode, the MN/MX pin is tied to VCC (logic high)
In this mode, the 8086 itself generates all bus control signals

## Slide 21: .

## Slide 22: MN / MX Pin 33 (Input)
8086 works in two modes:
Minimum Mode
Maximum Mode
If MN/MX is high, it works in minimum mode.
If MN/MX is low, it works in maximum mode.

## Slide 23: DT/R (Data Transmit/Receive) Pin 27 (Output)
This signal is used to decide the direction of data flow through the transceivers (bidirectional buffers)
When it is high, data is transmitted out by the processor
When it is low, data is received in by the processor
It is tristated during ‘hold acknowledge’ cycle.

## Slide 24: DEN (Data Enable) Pin 26 (Output)
This signal indicates the availability of valid data over the address/data lines.
It is used to enable the transceivers to separate the data from the multiplexed address/data signal.
It is active from the middle of T2 until the middle of T4.
It is tristated during ‘hold acknowledge’ cycle.

## Slide 25: ALE (Address Latch Enable) Pin 25 (Output)
This output signal indicates the availability of the valid address on the address/data lines.
It is used to demultiplex the address and data lines using external latches
That is to demultiplex the AD0-AD15 into A0-A15 & D0-D15 using external latches
It is active high and is never tristated.

## Slide 26: Cont.
The address bits are separated from the status bits using latches controlled by the ALE Signal

## Slide 27: Demultiplexing of address and data lines in 8086 processor

## Slide 28: M / IO Pin 28 (Output)
It is used to differentiate memory access and IO access.
When it is high, memory is accessed.
When it is low, I/O devices are accessed.
It is tristated during ‘hold acknowledge’ cycle.

## Slide 29: WR Pin 29 (Output)
It is a write control signal
It is asserted low whenever the processor writes data to memory or IO port

## Slide 30: INTA (Interrupt Acknowledge) Pin 24 (Output)
This is an interrupt acknowledge signal.
When microprocessor receives INTR signal, it acknowledges the interrupt by generating this signal.
The 8086 output is asserted low on this line to acknowledge when the interrupt request is accepted by the processor
It is active low during T2, T3 and Tw of each interrupt acknowledge cycle

## Slide 31: HOLD (Hold Request) Pin 31 (Input)
It is an input signal to the processor from other bus masters as a request to grant control of the bus.
It is usually used by the DMA controller to get the control of the bus

## Slide 32: HLDA (Hold Acknowledge) Pin 30 (Output)
It is an acknowledge signal by the processor to the master requesting the control of the bus through HOLD.
The acknowledge is asserted high when the processor accepts the HOLD, in the middle of the next clock cycle after completing the current bus (instruction) cycle.

## Slide 33: Minimum Mode 8086 System

## Slide 34: Cont.

## Slide 35: Two modes of 8086 Maximum Mode

## Slide 36: Maximum Mode Signals
For this mode, the MN/MX pin is tied to GND (logic low)

## Slide 38: RQ/GT1 and RQ/GT0 Pin 30 and 31 (Bi-directional)
These are bus request/bus grant pins
Other local bus masters request the processor through these lines to release the system bus.
After receiving the request, processor sends acknowledge signal on the same lines.
RQ/GT0 has higher priority than RQ/GT1.
These pins have internal pull-up resistors and may be left unconnected.

## Slide 39: S0, S1, S2 - Status Lines Pin 26, 27, 28 (Output)
These status signals indicate the type of operation being carried out by the microprocessor.
They are used by the 8288 bus controller to generate bus timing and control signals
These become active during T4 of the previous cycle and remain active during T1 and T2 of the current bus cycle.
The status lines return to passive state during T3 of the current bus cycle.

## Slide 40: Status Signals (S0, S1, S2) during various Machine Cycles

## Slide 41: LOCK Pin 29 (Output)
This output pin indicates that other system bus masters will be prevented from gaining the system bus, while this signal is low.
When it goes low, all interrupts are masked.
This pin is activated by using LOCK prefix on any instruction and remains active until the completion of the next instruction.

## Slide 42: QS1 and QS0 (Queue Status) Pin 24 and 25 (Output)
These pins provide the status of instruction queue.

## Slide 43: Maximum Mode 8086 System refer sl. 33

## Slide 44: Status Signals (S0, S1, S2) during various Machine Cycles

## Slide 45: Signals of the 8288
IORC – I/O Read Command
IOWC – I/O Write Command
MRDC – Memory Read Command
MWTC – Memory Write Command
AIOWC – Advance I/O Write Command
AMWTC – Advance Memory Write Command
INTA – Interrupt Acknowledge
DEN, ALE, DT/R

## Slide 46: Timing Diagram
Timing Diagram is a graphical representation.
It represents the execution time taken by each instruction in a graphical format.
The execution time is represented in T-states.
Instruction Cycle: The time required to execute an instruction
Machine Cycle: The time required to access the memory or input/output devices
T-State: A portion of an operation carried out in one system clock period

## Slide 47: T-State

## Slide 48: Timing Diagram
Timing diagram provides information about the various conditions of the signals while a machine cycle is executed.
In other words, it is the representation of various control signals generated during execution of an instruction
Following Buses and Control signals must be shown in a Timing diagram:
Higher Order Address Bus, Lower Address/Data bus, ALE,

## Slide 49: Bus cycle and T states

## Slide 50: Timing Diagram : Write cycle – Minimum mode

## Slide 51: Timing Diagram : Read cycle – Minimum mode

## Slide 52: Timing Diagram : Write cycle – Maximum mode

## Slide 53: Timing Diagram : Read cycle – Maximum mode

## Slide 54: References
Advanced Microprocessors and Peripherals by A K Ray & K M Bhurchandi
Microprocessors and Interfacing by Douglas V Hall & SSSP Rao

## Slide 55: Thank You