## Slide 1: MUNICIPAL SOLID WASTE MANAGEMENT 18CEO306T UNIT II

## Slide 2: Unit 2
Waste Generation and source reduction
Waste Stream Assessment (WSA)
Rationale for analysis Field investigation
Onsite segregation and resource recovery
Waste Generation and Composition
Waste Generation and Composition
Factors causing variation
Materials used for onsite storage containers
Source Reduction: Basics
Purpose and Implementation
Monitoring and Evaluation
Storage and collection of recyclables
Processing equipments for recycling
Material recovery facilities (MRF’s)
Significance of Recycling
Advantages and disadvantages in resource recovery
Tutorial 3: Source Reduction and Recycling in Bangalore:
Tutorial 4: Problems solving in recycling

## Slide 3
A waste stream assessment is the process of understanding the mix of material in the local waste stream. A waste stream assessment can be as simple as evaluating existing data that a local government already keeps or it may include an extensive waste sort to estimate quantities of various materials in the waste stream.
Waste stream is a tools can help you analyze your waste stream, realize profit opportunities in other's wastes, and determine the diversion programs that will most effectively help your local government meet and maintain its 50 percent goal.
WASTE STREAM ASSESSMENT (WSA)
Waste Stream Assessment:

## Slide 4
Importance of waste stream information
A waste stream assessment should not be conducted only to gather dust on a shelf. It should be a dynamic record that helps a local government prioritize its waste reduction activities.
A waste stream assessment provides local governments with the following benefits:
Identifies major material categories and their quantities in the waste stream.
Helps rank materials according to their impact on the local waste stream.
Helps identify specific commercial/industry types and/or facilities that should be targeted for waste reduction.
Assists in creating local educational materials on solid waste management.
WASTE STREAM ASSESSMENT (WSA)

## Slide 5
The growing world population is causing negative impacts on the planet. The current model of production and consumption generates a lot of waste that, in many cases, does not get reused or recycled.
For instance, in Europe, every citizen generates an average 1.69 kg of waste a day, i.e. 620 kg per year. Sixty percent of the volume of waste generated comes from packaging and product containers, often designed for just a single use.
WASTE GENERATION AND SOURCE REDUCTION
Waste Generation:

## Slide 6
The amount of generation of all waste, both hazardous and non-hazardous, generated by main groups of industries or sectors of the economy, expressed per capita and per unit of value added (in US $) by economic activity (at constant prices).
The recommended categories are based on the International Standard Industrial Classification of All Economic Activities Rev. 4 and include:
Manufacturing
WASTE GENERATION AND SOURCE REDUCTION

## Slide 7
Mining and quarrying
Construction
WASTE GENERATION AND SOURCE REDUCTION

## Slide 8
Electricity, Gas, steam and air conditioning supply;
Agriculture and forestry
WASTE GENERATION AND SOURCE REDUCTION

## Slide 9
All other economic activities
Households
WASTE GENERATION AND SOURCE REDUCTION

## Slide 10
Activities designed to reduce the volume or toxicity of waste generated, including the design and manufacturing of products with minimum toxic content, minimum volume of material, and/or a longer shelf life
WASTE GENERATION AND SOURCE REDUCTION
Source reduction:

## Slide 11
Reduction - Reduction in generation reduction in amount of material increase the lifetime of products eliminate the need for products
Reuse - no transformation being used for the same purpose again
Recycle - Use of the material as a source raw material, involves physical transformation
Recovery - Process to recover useful material from mixed waste (energy is an example)
WASTE GENERATION AND SOURCE REDUCTION
Source reduction:

## Slide 12: WASTE GENERATION AND SOURCE REDUCTION
Using durable coffee mugs.
Using cloth napkins or towels.
Refilling bottles.
Donating old magazines or surplus equipment.
Reusing boxes.
Turning empty jars into containers for leftover food.
Purchasing refillable pens and pencils.
Example of Source Reduction:

## Slide 13
The reasons for the analysis of waste composition, characteristics and quantity include the following:
It provides the basic data for the planning, designing and operation of the management systems.
An ongoing analysis of the data helps detect changes in composition, characteristics and quantities of wastes, and the rates at which these changes take place, which facilitates effective implementation of management systems.
It quantifies the amount and type of materials suitable for processing, recovery and recycling.
It provides information that helps in deciding appropriate technologies and equipment.
The forecast trends assist designers and manufacturers in the production of collection vehicles and equipment suitable for future needs.
RATIONAL ANALYSIS - FIELD INVESTIGATION

## Slide 14
Field investigations may take any one or a combination of the following forms:
Waste sorting: Sorting of wastes into predetermined components takes place at disposal sites for weighing and sampling in order to determine the percentage of each component and the physical and chemical characteristics of wastes.
It is carried out manually, and the sample size for analysis is between 100 and 150 kg. The implements required for the data for the planning, designing and operation of the purpose include sorting table, measuring box, bins or boxes to contain sorted materials and platform weighing machine. purpose include sorting table, measuring box, bins or boxes to contain sorted materials and platform weighing machine.
RATIONALE ANALYSIS - FIELD INVESTIGATION
Field Investigation

## Slide 15
Vehicle weighing: Vehicles are weighed when they enter the disposal sites loaded, and exit the sites empty. The vehicle’s front wheels are weighed first, followed by the rear wheels and the sum of the two gives the total weight.
Weighing is carried out each day of the weighing period in order to determine the average weight. The weighing of loaded and unloaded vehicles is accomplished with a weighing scale or weighbridge. Ideally, the weighing scale should be operated during the entire period of operation of the disposal site, round the clock, if necessary.
An electronic or a mechanical portable axle scale, with a capacity of 20 tonnes is suitable for the purpose. An electronic scale comprises two load-cell platforms and an electronic control and a display unit.
RATIONALE ANALYSIS -FIELD INVESTIGATION
Field Investigation:

## Slide 16
Field visits: This means visiting institutional and industrial sites to identify wastes being generated and disposal methods. Field visits involve visiting the facility, i.e., industry, institutions, etc., viewing the waste handling system and completing a questionnaire with the assistance of the plant manager or senior technical personnel who usually investigate wastes from industries and institutions. Collection of samples in sealed polythene bags follows for laboratory analysis to identify physical and chemical characteristics. Each sample may be in the range of 1.5 to 5 kg.
RATIONALE ANALYSIS -FIELD INVESTIGATION

## Slide 17
Waste segregation refers to the separation of dry and wet garbage, which paves the way for other concepts of waste management like composting, recycling and incineration.
India generates 62 million tonnes (MT) of waste every year, and only 43 MT is collected. Of the collected waste, close to 31 MT is dumped on landfill sites or water bodies and only11.9 MT is scientifically treated, disposed of in unauthorized places such as vacant plots, alleys, ditches, etc.;
Wet/Kitchen Waste:
This comprises of items like fruit peels, leftovers, vegetable skins, uncooked food, coffee or tea powder, and garden waste like leaves and twigs, Maintain a drum, container or a bin to deposit such waste, so that it can be converted into rich organic compost. You can choose your composting process. Examples include vermicomposting, aerobic and anaerobic composting.
ONSITE SEGREGATION AND RESOURCE RECOVERY
Onsite segregation:

## Slide 18
Dry waste:
Dry waste is divided into recyclable and non-recyclable waste. Items like used paper towels, hazardous chemical or food containers, foam materials, and dishware are some examples of dry waste that cannot be recycled or reused.
Dry recyclable waste includes pet bottles, plastic carry bags, newspapers, glass bottles, shoes, plastic cutlery, tires, cardboard, and so on.
If the recyclable waste is segregated further, it can fetch you money or goodies, local scrap dealers, recycling centres, raddiwalas to municipal corporations, there are several sources you can submit your dry waste to and get something in return.
ONSITE SEGREGATION AND RESOURCE RECOVERY

## Slide 19
Electronic waste Segregation:
There are three types of electronic waste you must be aware of:
Bulky: Fridge, microwave or anything is that is difficult to carry around.
Hazardous: Tubelights, light bulbs, toner cartridges, batteries, monitors and screens. Anything with a chemical component.
Non-hazardous: Cables, chargers, microwaves, gadgets like laptops and phones, there are several sources you can submit your dry waste to and get something in return.
Most of the offices follow a two-bin system—one for recyclable waste and one for wet garbage. But just like your home, the more you segregate, the better the waste management.
A bin for wet waste like leftover food, vegetable or fruit peels, tea bags, etc. in the canteen or cafeteria. If the volume of wet waste is vast, an office can also follow on-site composting.
ONSITE SEGREGATION AND RESOURCE RECOVERY

## Slide 20
Dry waste should be further divided into plastic, metal, glass and paper. Send each type of garbage every week to recycling centre's or services.
Electronic waste like CDs, pen drives, bulbs, tube-lights, computer systems, electric cables, keyboards, batteries, motherboards etc. should be collected by the office and transported to e-waste collection centre's.
Bins should be placed in bathrooms for sanitary waste like pads. Some offices even install incinerators to treat it at the source.
ONSITE SEGREGATION AND RESOURCE RECOVERY

## Slide 21
Waste generation encompasses those activities in which waste, be it solid or semi-solid material, no longer has sufficient economic value for its possessor to retain it.
The processing of raw materials is the first stage when wastes are generated, and waste generation continues thereafter at every step in the process as raw materials are converted into final products for consumption.
In below flowchart suggests that we can reduce the amount of solid waste by limiting the consumption of raw materials and increasing the rate of recovery and reuse.
There needs to be, therefore, a societal change in the perception of wastes. This sounds simple. But, implementing changes in the society is difficult, unless appropriate management solutions are provided.
WASTE GENERATION AND COMPOSITION
Waste Generation:

## Slide 22
WASTE GENERATION AND COMPOSITION
Waste Generation:

## Slide 23
WASTE GENERATION AND COMPOSITION
Waste Generation:

## Slide 24
Some of the general observations associated with the composition of wastes include the following:
The major constituents are paper and decomposable organic materials.
More often than not, metal, glass, ceramics, textile, dirt and wood form part of the composition, and their relative proportion depends on local factors.
Average proportions of the constituents reaching the disposal sites are consistent and urban wastes are fairly constant although subject to long-term changes such as seasonal variations.
MSW composition in India is approximately 40%–60% compostable, 30%–50% inert, and 10%–30% recyclable. According to the National Environmental Engineering Research Institute (NEERI), Indian waste consists of 0.64%±0.8% nitrogen, 0.67%±0.15% phosphorus, and 0.68%±0.15% potassium, and has a 26±5C:N ratio
WASTE GENERATION AND COMPOSITION
Waste Composition:

## Slide 25
Waste composition also varies with socio-economic status within a particular community, since income determines life-style – consumption patterns and cultural behavior.
Several conclusions may be drawn from this comparative data: · The proportion of paper waste increases with increasing national income; · The proportion of putrescible organic matter (food waste) is greater in countries of low income than those of high income.
Variation in waste composition is more dependent on national income than geographical location, although the latter is also significant; · Waste density is a function of national income, being two to three times higher in the low-income countries than in countries of high income; · Moisture content is also higher in low-income countries; and · The composition of waste in a given urban center varies significantly with socio-economic status (household income).
The detailed Waste composition were discussed Table 1. Waste Composition
WASTE GENERATION AND COMPOSITION
Waste Composition:

## Slide 26
WASTE GENERATION AND COMPOSITION

## Slide 27
Source reduction /Recycling
Geographic location
Season
Frequency of collection
Legislation
Public attitudes
Per capita income
Size of households
Population density
Historical / Tourist places
Typically population increase explains 1/3 of increase in MSW generation
FACTORS CAUSING VARIATION
Refer : https://doi.org/10.1098/rsos.160764

## Slide 28
Geographic location: The influence of geographic location is related primarily to different climates that can influence both the amount of certain types of solid wastes generated and the collection operation. For instance, substantial variations in the amount of yard and garden wastes generated in various parts of India are related to the climate. To illustrate, in the warmer southern areas, where the growing season is considerably longer compared to the northern areas, yard wastes are collected in considerably larger quantities and over a longer period of time.
Seasons: Seasons of the year have implications for the quantities and composition of certain types of solid wastes. For example, the growing season of vegetables and fruits affect the quantities of food wastes.
FACTORS CAUSING VARIATION

## Slide 29
Collection frequency: A general observation is that in localities, where there are ultimate collection services, more wastes are collected. Note that this does not mean that more wastes are generated. For example, if a homeowner has access to only one or two containers per week, due to limited container capacity, he or she will store newspapers or other materials in some specified storage area.
However, the same homeowner will tend to throw them away, if there is access to unlimited container services. In this latter situation, the quantity of waste generated may actually be the same but the quantity collected, as it relates to the frequency of collection, is considerably different.
FACTORS CAUSING VARIATION

## Slide 30
Legislation: This refers to the existence of local and state regulations concerning the use and disposal of specific materials and is an important factor that influences the composition and generation of certain types of wastes. The Indian legislation dealing with packing and beverage container materials is an example.
Public attitudes: Significant reduction in the quantity of solid waste is possible, if and when people are willing to change – on their own volition – their habits and lifestyles to conserve the natural resources and to reduce the economic burden associated with the management of solid wastes.
Per capita income: The characteristics of the population influence the quantity and composition of waste generated. The amount of waste generated is more in low-income areas compared to that in high-income areas. Similarly, the composition differs in terms of paper and other recyclables, which are typically more in high-income areas as against low-income areas
FACTORS CAUSING VARIATION

## Slide 31
Waste storage encompasses proper containers to store wastes and efficient transport of wastes without any spillage to transfer stations/disposal sites.
Garbage and refuse generated in kitchens and other work areas should be collected and stored in properly designed and constructed water-proof garbage cans (waste bins). The censor receptacles can be constructed from galvanized iron sheet or plastic materials. They should have tightly fitting covers.
They must be of such size that, when full, they can be lifted easily by one man. They should be located in a cool place on platforms at least 30 centimeters above ground level. After putting in garbage, they should be. An adequate number of suitable containers should be provided with proper platforms with receptacles stand. The number may depend on the amount, type and establishments where the need arises. Suitable containers should be watertight, rust resistant, with tight-fitting covers, fire-resistant, adequate in size, light in weight, with side handles and washable.
MATERIALS USED FOR ONSITE STORAGE CONTAINERS

## Slide 32
MATERIALS USED FOR ONSITE STORAGE CONTAINERS

## Slide 33: SOURCE REDUCTION
Source reduction, also known as waste prevention, is an approach that precedes waste management and addresses how products are manufactured and, purchased.
Reducing waste before it is generated is a logical way to save costs and natural resources, and preserve the local environment

## Slide 34: SOURCE REDUCTION
The activities that reduce the amount of waste generated at source as well as activities that involve any change in the design, manufacture, purchase or usage of materials/products to reduce their volume and/or toxicity, before they become part of the solid waste stream
Successful implementation of source reduction programme requires the co-operation of all stakeholders, (e.g., businesses, industries, consumers and state and local governments).

## Slide 35: SOURCE REDUCTION

## Slide 36: SOURCE REDUCTION
Source reduction programme should be part of a community waste management plan. Source reduction activities vary widely and many factors have to be considered while evaluating them.

## Slide 37: VIDEO
https://www.youtube.com/watch?v=DmFGsxLcT6k

## Slide 38: PURPOSE OF SOURCE REDUCTION
Product reuse
Material volume reduction
Toxicity reduction
Increased product lifetime
Decreased consumption

## Slide 39: PURPOSE OF SOURCE REDUCTION
Product reuse: Using reusable products, instead of their disposal equivalents, reduce the amount of materials that are to be managed as wastes. An example of product reuse is the reusable shopping bag.
Material volume reduction: Reducing the volume of material used changes the amount of waste entering the waste stream. This helps in controlling the waste generated and its disposal. For example, buying in bulk or using large food containers reduces the amount of packaging waste generated.

## Slide 40: PURPOSE OF SOURCE REDUCTION
Toxicity reduction: Source reduction reduces the amount of toxic constituents in products entering the waste stream and reduces the adverse environmental impacts of recycling or other waste management activities.
For example, substitution of lead and cadmium in inks (solvent-based to water based) and paints is a source reduction activity.
Increased product lifetime: Source reduction facilitates the use of products with longer lifetime over short-lived alternatives that are designed to be discarded at the end of their useful lives. Put differently, it encourages a product design that allows for repair and continued use rather than disposal. Manufacturing long-life tyres is a good example of increasing product lifetime.

## Slide 41: PURPOSE OF SOURCE REDUCTION
Decreased consumption: This refers to the reduced consumption of materials that are not reusable (e.g., using a reusable shopping bag instead of picking up plastic bags from the store).
Consumer education about the materials that are difficult to dispose of or are harmful to the environment is essential. Buying practices can thus be altered (e.g., buying in bulk) to reflect environmental consciousness.

## Slide 42: ADVANTAGES OF SOURCE REDUCTION
Reduction in extent of environmental impacts
Reduction in resource consumption and generation of pollution
It includes producer, consumer, prudent and efficient activities

## Slide 43: IMPLEMENTATION
Education and research
Financial incentives and disincentives
Regulation

## Slide 44: IMPLEMENTATION
Education and research: Consumers, businesses, industries, schools, etc., can implement education and research activities to address the need for source reduction, its consequences, available choices, benefits and costs.
Essentially, the aim of such education and research activities is to provide and develop information about source reduction goals, needs and methods and to elicit voluntary efforts from the public and private sectors to help bring about some specific changes

## Slide 45: EDUCATION AND RESEARCH
Developing curricula for schools and universities
Exploring and developing funding sources.
Developing media campaign
Forming stakeholder councils.

## Slide 46: IMPLEMENTATION
Financial incentives and disincentives: Linking an economic benefit to the implementation of source reduction activities encourages source reduction.
For example, financial disincentives represent additional costs to the waste producing activities that could be avoided through source reduction activities.

## Slide 47: FINANCIAL INCENTIVES AND DISINCENTIVES
01
02
03
04
Tax credit or exemption
variable waste disposal charges for garbage collection
Graduated fee structure for garbage collection
Product disposal charges

## Slide 48: IMPLEMENTATION
Regulation: Although most regulation occurs at the national and state level, local authorities can participate in legislative activities in developing regulations that affect municipal SWM.
It is possible, for example, to establish a programme to inform the consumers about environmental impacts, durability, reusability and recyclability of products as well as to declare source reduction as a top priority in SWM.

## Slide 49: REGULATION
Quantity control regulation
Product design regulation

## Slide 50: RECYCLE MATERIALS
Recycling is the process of converting waste materials into new materials and objects.
The recovery of energy from waste materials is often included in this concept. The recyclability of a material depends on its ability to reacquire the properties it had in its virgin or original state.

## Slide 51: STORAGE AND COLLECTION OF RECYCLABLES
Collection of source-separated materials is a necessary component of recycling programme. Establishing a collection system for source-separated materials will require more careful planning than regular trash collection.
Resident convenience
Collection crew convenience
Cost effectiveness
Integrity of materials

## Slide 52: STORAGE AND COLLECTION OF RECYCLABLES
Resident convenience: The easier it is for residents to separate materials, the higher the participation and recovery rates will be higher.
Collection crew convenience: The system should be convenient for collection crews. For example, loading and sorting activities should be as simple as possible.
Cost effectiveness: Equipment and procedures must be designed to maximize collection crew and vehicle productivity.
Integrity of materials: The storage and collection system should keep recyclables in the best shape possible. It should be properly handled, dry and contaminant free.

## Slide 53: STORAGE AND COLLECTION OF RECYCLABLES

## Slide 54: PROCESSING EQUIPMENT FOR RECYCLING
Recycling involves a number of processing techniques and these processes require different equipment's. However, some of the special equipment's used in recycling are
Balers
Can densifiers
Glass crushers
Magnetic separators
Wood grinders
Scales

## Slide 55
Balers: Balers can be used to densify many types of materials including paper, cardboard, plastics and cans. Balers can improve space utilization and reduce material transportation costs.
Can densifiers: Can crushers are used to densify aluminum and steel cans prior to transport.
PROCESSING EQUIPMENT FOR RECYCLING

## Slide 56
Glass crushers: These are used to process glass fraction separated by color and break it into small pieces. This crushed material is then called cullet, and can be reprocessed into new glass products.
Magnetic separators: These are used to remove ferrous material from a mixture of materials.
PROCESSING EQUIPMENT FOR RECYCLING

## Slide 57: PROCESSING EQUIPMENT FOR RECYCLING
Wood grinders: These are chippers and are used to shred large pieces of wood into chips that can be used as mulch or as fuel.
Scales: These are used to measure the quantity of materials recovered or sold.

## Slide 58: MATERIAL RECOVERY FACILITIES (MRF)
MRF is a centralized facility that receives, separates, processes and markets recyclable material. It can be operated with both drop off and curbside programmes. The primary advantage of MRF is that it allows materials directly from the municipalities and processes them uniformly. It is generally designed to handle all type of recyclables. Implementation of MRF in a municipality depends upon a number of factors as follows,
Market demand
Separate collection
Number of different recyclables
Quantities of materials

## Slide 59: MATERIAL RECOVERY FACILITIES (MRF)
Market demand: When additional processing is required, MRF is more useful as buyers may have certain material specifications.
Separate collection: In systems that require residents to separate their recyclables, intermediate separation and processing is required.
Number of different recyclables: In general, a MRF will be more beneficial when a large number of different recyclables are collected.
Quantities of materials: Because MRF involves substantial capital and operating costs (e.g., buildings, equipment and labour), it is expected to handle a significant amount of materials to justify its operation.

## Slide 60: SIGNIFICANCE OF RECYCLING
Recycling is one of the fundamental parts of the waste management plan.
Although it alone cannot solve a community’s municipal SWM problem, it can divert a significant portion of waste stream from disposal in landfill and combustion facilities.
Recycling has a lot of direct and indirect significance for the society

## Slide 61: SIGNIFICANCE OF RECYCLING
Economic significance
  Cost reduction
  Employment
  Energy saving
  Reduced health care costs
Environmental and health significance
  Improved environment
  Natural resource conservation
Social significance

## Slide 62: SIGNIFICANCE OF RECYCLING
Economic significance: Economic assessment of waste recycling is a difficult task as many of the beneficial environmental and social impacts of recycling are long-term and are intangible, and, therefore, are difficult to quantify.
Cost reduction: Resource recovery through recycling of solid waste could be of interest to waste management authorities as a means of reducing the waste disposal cost.

## Slide 63: SIGNIFICANCE OF RECYCLING
  Employment: Recycling of waste is a labour intensive activity, and its potential to ease the unemployment problem is high.
  Energy saving: Use of recyclables in some industrial processes is known to consume less energy than the use of any other raw material.
  Reduced health care costs: Improved health and sanitary conditions in urban areas resulting from indirect benefits of waste recycling can reduce the investment in public health programme.
  Saving costs for other public utilities: Enhanced solid waste recycling practices can reduce the frequency of sewer clogging, blocking of natural watercourses and pollution of water bodies.

## Slide 64: SIGNIFICANCE OF RECYCLING
Environmental and health significance: The volume of waste is increasing rapidly because of population growth and economic development.
The composition of waste is also changing, leading to waste production with more recyclables. At the same time, polluted waste fractions are increasing because of increasing complex processes being used in industries, and these contribute increasingly to environmental degradation.

## Slide 65: SIGNIFICANCE OF RECYCLING
  Improved environment: The environmental pollution may be due to inadequate SWM as well as due to its effect on other urban infrastructure.
  Recycling reduces the volume of waste that has to be finally dumped, and thereby causing reduction in pollution at the waste disposal sites
  Natural resource conservation: Industries with natural products as their raw material for production are depleting natural resources.
  Use of more and more recyclable solid wastes in industrial production will relieve the tremendous pressure on these precious resources

## Slide 66: SIGNIFICANCE OF RECYCLING
Social significance: People engaged in waste collection activities are normally of low social and economic standing. This is especially true with scavengers, which is evident from persisting poor quality of their living and working conditions.
Different groups of people engaged in waste recycling have a hierarchical social and economic status, in which, processors are at the top of the hierarchy followed by waste dealers and wholesalers, waste buyers and waste collectors in that very order, while scavengers are at the bottom.

## Slide 67: ADVANTAGES AND DISADVANTAGES IN RESOURCE RECOVERY
Recycling helps to reduce energy usage, reduce the consumption of fresh raw materials, reduce air pollution and water pollution (from landfilling) by reducing the need for “conventional” waste disposal and also reduces greenhouse gas emissions.

## Slide 69: ADVANTAGES OF RECYCLING
  1. Recycling minimizes pollution
  2. Protects the environment
  3. Recycling minimizes global warming
  4. Conserves natural resources
  5. Recycling cuts down the amount of waste in landfill sites
  6. Recycling ensures sustainable use of resources
  7. Recycling contributes to the creation of jobs
  8. Reduces energy consumption
  9. Recycling helps to make and to save money
  10. Recycling spreads environmental awareness
  11. Recycling can reduce allied activities needed for the production of fresh products
  12. Recycling of organic matter
  13. Innovations drive scientific advancements

## Slide 70: DISADVANTAGES OF RECYCLING
  1. High upfront capital costs
  2. Recycling sites are always unhygienic, unsafe and unsightly
  3. Products from recycled waste may not be durable
  4. Recycling might not be inexpensive
  5. Recycling is not widespread on large scale
  6. More energy consumption and pollution
  7. Result in pollutants
  8. Increased processing cost and low-quality jobs
  9. Stricter and more stringent implementation required
  10. Recycling is still ineffective
  11. Methane is a GHG
  12. Revenue loss

## Slide 71: CASE STUDY: SOURCE REDUCTION AND RECYCLING IN BANGALORE

## Slide 72: CASE STUDY: SOURCE REDUCTION AND RECYCLING IN BANGALORE
Source reduction, including reuse and recycling, can help reduce waste disposal and handling costs, because it avoids the costs of municipal composting, land filling and combustion.
Source reduction also conserves resources and reduces pollution, including greenhouse gases that contribute to global warming. Waste reduction, reuse and recycling, thus, play an important role in SWM.

## Slide 73: CASE STUDY: SOURCE REDUCTION AND RECYCLING IN BANGALORE
In Bangalore, 66% of the waste generated is collected for recovery, i.e., about 2,373 tonnes per day. While 722 tonnes per day is reused, the rest (i.e., 1,450 tonnes) goes for recycling.
The agents involved in the collection and recovery of wastes in the city include waste pickers, IWB (i.e., itinerant waste buyer), middlemen (or intermediaries), the municipality and recycling units (both large and small).
While the three agents in the informal sector and the municipality are directly involved in waste collection activities, the waste is processed by the recycling units, which receive recyclable waste from middlemen and municipality.
Of the 1450 tonnes collected for recycling, 1077.8 tonnes come from intermediaries, 60.4 come from IWB and 312 tonnes come from waste pickers. This amounts to 40% of the total waste (i.e., 3613 tonnes per day) generated.