## Slide 1: Role of SDN in 5G- Drawback of hardware-based network functions., Network Functions Virtualization (NFV) and Software Defined Networking (SDN) in 5G, optimization models that aim at finding the optimal design for a mobile core network based on SDN and NFV

## Slide 2: Role of SDN in 5G- Drawback of hardware-based network functions.
With the rapid growth of user traffic, service innovation, and the persistent necessity to reduce costs, today’s mobile operators are faced with several challenges.
In networking, two concepts have emerged aiming at cost reduction, increase of network scalability and deployment flexibility, namely Network Functions Virtualization (NFV) and Software Defined Networking (SDN)
NFV mitigates the dependency on hardware, where mobile network functions are deployed as software virtual network functions on commodity servers at cloud infrastructure, i.e., data centers. Hence, NFV is expected to reduce the cost of mobile networks
SDN provides a programmable and flexible network control by decoupling the mobile network functions into control plane and data plane functions.
The design of the next generation mobile network (5G) requires new planning and dimensioning models to achieve a cost optimal design that supports a wide range of traffic demands.
SDN enables a centralized control view that provides the operators with the possibility to achieve more efficient network control

## Slide 3: SDN and NFV Mobile Network Architectures, Dimensioning and Resource Allocation Problems

## Slide 4
There are two main areas of modeling and optimization related to the use of SDN and NFV in the mobile core network:
(a) placement of SDN controllers and switches &
(b) resource allocation and placement of VNFs.
The dimensioning and placement of SDN controllers and switches is known as the controller placement problem.

## Slide 5
The mobile core network, in the latest LTE standard [34], shown in Fig. 1a,
The core network functions can be classified into two categories based on their purpose: (a) functions that handle the control plane only, such as the Mobility Management Entity (MME) or the Home Subscriber Server (HSS) (b) functions that handle both data as well as control planes, such as the Serving Gateway (SGW) and the Packet Data Network Gateway (PGW).
The data plane functions implement special purpose processing for mobile networks, i.e., GTP tunneling for the user data in order to differentiate between the users and to be able to provide service quality classes for each user.
Other data plane functions include charging and accounting for the user data usage. The control plane functions handle the setup of the user tunnels and mobility management, i.e., tracking area updates and redirection of user tunnels. Additionally, control functions handle user authentication, subscription management and as access control.

## Slide 6
In the current LTE mobile core network, what we refer to as legacy, the data and control plane functions are realized by dedicated hardware that implements each specialized function.
Moving towards the next generation 5G mobile core network, functions that only handle the control plane, e.g., MME, could be deployed as virtual network functions, i.e., software, on a cloud infrastructure, i.e., data centers.
However, regarding the functions that handle both the data as well as control planes, i.e., SGW and PGW, we consider the two realization options, either SDN based or NFV based

## Slide 7
Considering an SDN based deployment, shown in Fig. 1b, the control plane mobile core functions run as VNFs while the gateway functions, i.e., SGW and PGW, are decoupled into SDN controllers (S/PGW CTR) and special purpose SDN+ switches, as shown in Fig. 1b. The SDN controllers, deployed at the data center infrastructure, configure the SDN+ switches which handle the data plane traffic.
The controllers implement the control plane of the core network gateway functions.
SDN controllers are required to handle the LTE control plane signaling procedures which are defined by the 3GPP standard, i.e., exchange of signaling messages with the radio access network in order to support the user’s attachment to the mobile network or user’s mobility

## Slide 8
According to the signaling procedures, the controllers are responsible to configure the data plane, i.e., SDN+ switches, via the SDN API used by the operator. Additionally, the controllers need to collect the data usage of each user from the data plane switches for the purpose of charging and accounting.
On the other hand, the SDN+ switches implement the gateway data plane functions. One important data plane function needed at the SDN+ switches is GTP tunneling which is used to identify data plane traffic of users.
The SDN+ switches monitor the data plane statistics for charging and accounting. Additionally, the SDN+ switches need to support the configuration of quality of service classes that can be assigned to users.

## Slide 9
In case of an NFV based deployment, as illustrated in Fig. 1c, the control plane mobile core functions as well as the gateway functions, i.e., SGW and PGW, run as VNFs (vS/PGW) on commodity hardware at data centers.
This means that the gateway’s control plane as well as the data plane processing is running on commodity servers in the cloud.
The data plane processing on commodity servers can be accelerated by solutions such as Intel DPDK
the legacy core network hardware would be replaced by simple forwarding switches, i.e., transport switches, that forward both the data plane and control plane traffic between the radio access network, the data centers and the external network, as illustrated in Fig. 1c.

## Slide 10
Note that in this architecture, all mobile core network functions are migrated to software running on commodity servers and are fully independent from hardware, i.e., functions which handle control plane only, e.g., MME, and functions that handle both data as well control plane, e.g., SGW and PGW.
This implies that there is no processing, i.e., function, implemented on the forwarding switches of the mobile core network.

## Slide 11: Control Plane Function Chains Analysis, requirements & challenges of SDN and NVF In 5G

## Slide 12: Control Plane Function Chains Analysis
The LTE control plane procedures in the mobile core network consist of multiple sequential iterations between the network functions. For instance, the ATTACH procedure, the 3GPP standard , involves mainly the MME, SGW and PGW for the setup of a user GTP tunnel.
The ATTACH procedure defines the control messages exchanged in order to attach a user to the mobile network and setup its data plane GTP tunnel.
It includes 3 control iterations between the RAN and the MME, 2 control iterations between the MME and the SGW and 2 control iterations between the SGW and PGW, respectively. Hence, the control plane is required to be modeled differently from how the control plane is modeled in traditional IP networks

## Slide 13
Considering an SDN deployment for the mobile core gateway functions, the control plane function chains would be mapped on the path between the RAN, i.e., eNBs, and the data centers which run the virtual control functions, i.e., vMME and the SDN controllers
This makes the control plane latency dependent on the location of the data centers. The control function chains are also extended by the control path between the SDN controllers and their respective SDN+ switches. Whereas, an NFV deployment means that the mobile core VNFs are all consolidated in data centers
Hence, the control plane function chains are mapped on the path between the RAN and the data centers infrastructure. Therefore, the latency of the control plane function chains becomes dependent only on the locations of the data centers.

## Slide 14: Data Plane Function Chains Analysis
The data plane path within the mobile core depends on the operator’s decision for the realization of both the SGW and PGW functions. In case of using SDN, as shown in Fig. 1b, the legacy hardware functions would be replaced with the SDN+ switches which are controlled by the controllers residing in the cloud.
This means that the data plane itself would follow the same function chains as the legacy network, i.e., between the SDN+ switches. It also means that the data plane latency
depends only on the locations of the SDN+ switches and is decoupled from the location of the data center infrastructure.
The data plane traffic in mobile networks can be modeled as uni-directional function chains, i.e., uplink or downlink

## Slide 15
On the other hand, following the concept of NFV, the SGW and PGW functions are moved to the cloud. The legacy functions are replaced by simple forwarding transport switches, as
shown in Fig. 1c, which transport the data plane traffic towards the data center infrastructure where the data plane processing is carried out by the software gateway functions.
This means that the NFV architecture has an impact on the data plane latency as it changes the data plane function chains.
The data plane function chains are extended by the links carrying the traffic back and forth between the transport switches and the data centers.
Hence, the data plane latency becomes dependent on the data center locations.

## Slide 16: Requirements & challenges of SDN and NVF In 5G
Fig. 1 describes the concept in the already presented SDN architectures, which are based on decoupling the data and control layers.
The infrastructure layer includes commodity switches. The control layer includes a cluster of controllers.
The application layer includes applications and network appliances. Firewalls are virtually deployed reclaiming the NFV and function in the application layer
The general concept of SDN architectural model

## Slide 17
The main requirements and challenges linked to the SDN and NFV

## Slide 18: Existing Solutions, future directions

## Slide 19
1) OpenRadio: describes the programmable data plane in wireless systems and its possible implementation in today’s mobile networks. Firstly, there are several analyses including the cell-based optimization, the coexistence of heterogeneous and alternative types of cells and the application of specific wireless services.
It introduces programming abstractions, such as modular declarative interface, information plane, state machine model and deadlines. Finally, it refers to the challenges of the OpenRadio and suggests a designing policy.
2) OpenRAN: introduces an OpenRAN approach via virtualization. The suggested overall protocol is divided in the SDN controller, in the wireless spectrum resource and the cloud computing resource protocol. It also induces four levels of virtualization: application, cloud, spectrum and cooperation. It concludes that controllers and programmable schemes achieve routing and bandwidth allocation and several flow priorities
Existing Solutions

## Slide 20
3) SoftRAN: introduces the dense network management. The authors design the SoftRAN (Software defined RAN) combined with a coupled control plane in dense networks. It introduces the base station abstraction, the SoftRAN, the controller architecture and the refactoring of the control plane. It ends up indicating the feasibility of RAN.
4) NetShare: operates as manager of shared resources and is introduced as a way of reallocating the existing resources of base stations and multiple entities in an existing network. Netshare isolates entities and highly utilizes the resources of an entity. The resource allocation is based on distribution, strict isolation, network heterogeneity and per base station reservation.

## Slide 21
5) ONOS: analyzes the SDN based on ONOS and the motivation linked to wireless transport networks. MCORD (Mobile CORD) is the mobile ONOS CORD and is available for experimentation since the Emu release of ONOS.
6) Software Defined Cellular Network (SDCN): includes fundamental answers in the already augmenting demands, namely flexible policies, scalability, commodity switches, remote control of base stations. Several controller applications are directing traffic throughout middleboxes, monitoring network controlling and billing, providing seamless subscriber mobility and QoS, accessing control policies, offering virtual cellular operators and managing inter-cell interference.
Last but not least, slicing several resources, such as bandwidth, topology, traffic, device CPU and forwarding tables is important for efficient resource allocation.

## Slide 22
7) Cellular SDN (CSDN): focuses on flexible policies on subscriber attributes, scalability through local agents, flexible switch patterns and actions and network virtualization on subscriber attributes. There are also several CSDN applications such as flexible subscriber policies, scalability for local agents, flexible switch patterns and virtualization of the subscriber attributes.
The SDN architecture induces logical centralized control, programmability and high abstraction levels . The background study is based on inter-cell interference management and mobile traffic management.
SDN and NFV are capable of providing intelligent services and dynamic resource allocation. The virtualized network in SDN architectures includes several functions, designing considerations in the forwarding and control plane.
Practical questions are considered when it comes to centralized vs distributed data collection, data processing, decision making and user privacy. Future work is summarized as being a combination of CSDN with Big Data.

## Slide 23
8) Wireless SDN (WSDN): introduces a wireless SDN architecture. The virtualization of several functions and mechanisms of the network infrastructure are analyzed alongside with other important issues, such as sharing, virtualizing core servers, dynamic energy policies. SDN, OpenFlow, CAPWAP and reconfigurable wireless devices are defined.
Virtualization matters, QoE-aware network operations, network access selection and mobility control are raised.
9) SDN Mobile Cloud: offers important benefits in wireless communications alongside with novel applications, that STEM from SDN. There is a consideration of several challenges of combining SDN with adhoc networks and an heterogeneous architecture is proposed.

## Slide 24
10)Mobile Extension of SDN (MeSDN): summarizes the possible mobile cloud requirements. MeSDN should be used at the enterprises to cover the augmenting demands of the visitors in using the network. The proposed architecture describes the flow manager, the roles of the local and the global controllers.
There is also a reference in MeSDN applications, such as App-aware End to End (E2E), QoS, network fault diagnosis, WLAN Virtualization, 4G cellular networks. It introduces pTDMA (pseudo Time Division Multiple Access), a type of pseudo TDMA, analyzing scheduling principles, downlink control, power saving, prototype implementation, such as architecture, threats, evaluation.
The most important challenges are presented, among which are: millisecond level synchronization, driver buffering delay and 802.11 beacons.

## Slide 25: FUTURE WORKS
A. CROSS LAYER CONTROLLER
Service-oriented services represent that, each service will be one of the factors that affect the policy, as different services or applications have different features, which directly reflect the habits of using network resources.
For example, network traffic of viewing web pages may be intermittent or video conferencing must use a lot of bandwidth during a xed period of time.
The SDN Layer can be used to collect the information, and algorithms are applied to analyze the optimal allocation of spectrum and bandwidth, and then change the policy SDN Layer.
B. ENERGY-AWARE
The future is a green computing world, with mobile devices as the mainstay. However, limited battery power remains an indisputable fact. When consumers are accessing a network, if they are requested to provide power consumption information to the Cross Layer Controller as the goal of the algorithm, it can save power consumption. Maintaining a good QoS is the main challenge.

## Slide 26
C. SECURITY
The web services are provided by ISPs, and the users need to follow the norms of spectrum access. However, as CR is a client-oriented technology, how to avoid illegal use of others' frequency will be a major issue.
The SDN Controller documents the frequency information and use conditions of each user; therefore, control of SDN and privacy issues should be discussed.
In addition, SDR also has security issue such as that the attackers may try to interfere other users or stealing the spectra resource