## Slide 1: UNIT I – BASICS OF SDN
Introduction to Open Flow
Wire Protocol
Replication
FAWG (Forwarding Abstraction Workgroup)
Reference: Ref. 2, Ch. 3 (Page. 47 to Page 57)
UNIT I – SESSION 1
SESSION 8

## Slide 2: Introduction to Open Flow

## Slide 3: Open Flow
OpenFlow was originally imagined and implemented as part of network research at Stanford University.
Its original focus was to allow the creation of experimental protocols on campus networks that could be used for research and experimentation.
Prior to that, universities had to create their own experimentation platforms from scratch.
What evolved from this initial kernel of an idea was a view that OpenFlow could replace the functionality of layer 2 and layer 3 protocols completely in commercial switches and routers.
This approach is commonly referred to as the clean slate proposition.

## Slide 4: Open Flow
In 2011, a nonprofit consortium called the Open Networking Foundation (ONF) was formed by a group of service providers to commercialize, standardize, and promote the use of OpenFlow in production networks.
The ONF is a new type of Standards Development Organization in that it has a very active marketing department that is used to promote the OpenFlow protocol and other SDN-related efforts.
The organization hosts an annual conference called the Open Networking Summit as part of these efforts.
In the larger picture, the ONF has to be credited with bringing attention to the phenomenon of software-defined networks.

## Slide 5: Key Components of Open Flow Model
The key components of the OpenFlow model, as shown in Figure, have become at least part of the common definition of SDN, mainly:
• Separation of the control and data planes (in the case of the ONF, the control plane is managed on a logically centralized controller system).
• Using a standardized protocol between controller and an agent on the network element for instantiating state (in the case of OpenFlow, forwarding state).
• Providing network programmability ( the capability of configuring and managing network devices and services using software-based methods rather than traditional manual configuration) from a centralized view via a modern, extensible API.

## Slide 6: Key Components of Open Flow Model
OpenFlow is a set of protocols and an API (An API (Application Programming Interface) is a set of rules and protocols for building and interacting with software applications.)
Put another way, the controller does nothing without an application program giving instructions on which flows go on which elements.

## Slide 7: OpenFlow protocols are currently divided in two parts:
A wire protocol (currently version 1.3.x) for establishing a control session, defining a message structure for exchanging flow modifications (flowmods) and collecting statistics, and defining the fundamental structure of a switch (ports and tables).
A configuration and management protocol, of config (currently version 1.1) based on NETCONF (NETCONF(Network Configuration Protocol) is a protocol defined by the IETF to “install, manipulate, and delete the configuration of network devices) to allocate physical switch ports to a particular controller, define high availability (active/standby) and behaviors on controller connection failure.
Though OpenFlow can configure the basic operation of OpenFlow command/control it cannot (yet) boot or maintain (manage in an FCAPS context) an element.

## Slide 8: Wire Protocol
The OpenFlow Wire Protocol is a fundamental component of the OpenFlow specification, which plays a key role in Software-Defined Networking (SDN). This protocol defines the communication between an OpenFlow controller and an OpenFlow-compatible switch, allowing for dynamic network management and configuration.
First, it introduces the concept of substituting ephemeral state (flow entries are not stored in permanent storage on the network element) for the rigid and unstandardized semantics of various vendors’ protocol configuration.
For most network engineers, the ultimate result of such configuration is to create forwarding state (albeit distributed and learned in a distributed control environment).
In fact, for many, the test of proper configuration is to verify forwarding state (looking at routing, forwarding, or bridging tables).
Of course, this shifts some of the management burden to the controller(s)—at least the maintenance of this state versus the distributed management of configuration stanzas on the network elements.

## Slide 9: Wire Protocol
Second, in an OpenFlow flow entry, the entire packet header (at least the layer 2 and layer 3 fields) are available for match and modify actions, as shown in Figure.
Many of the field matches can be masked.
These have evolved over the different releases of OpenFlow.
Figure illustrates the complexity of implementing the L2+L3+ACL forwarding functionality (with next hop abstraction for fast convergence) can be.
The combination of primitives supported from table to table leads to a very broad combination of contingencies to support.

## Slide 11: Wire Protocol
The OpenFlow protocol is extensible through an EXPERIMENTER extension (which can be public or private) for control messages, flow match fields, meter operation, statistics, and vendor-specific extensions (which can be public or private).
Table entries can be prioritized (in case of overlapping entries) and have a timed expiry (saving clean-up operation in some cases, and setting a drop dead efficacy for flows in one of the controller loss scenarios).
OpenFlow supports PHYSICAL, LOGICAL, and RESERVED port types. These ports are used as ingress, egress, or bidirectional structures.

## Slide 12: Reserved Ports
The RESERVED ports IN_PORT and ANY are self-explanatory.
TABLE was required to create a multitable pipeline (OpenFlow supports up to 255 untyped tables with arbitrary GoTo ordering).
The remaining RESERVED ports enable important (and interesting) behaviors.
Logical Ports
LOCAL An egress-only port, this logical port allows OpenFlow applications access ports (and thus processes) of the element host OS.
NORMAL An egress-only port, this logical port allows the switch to function like a traditional Ethernet switch (with associated flooding/learning behaviors). According to the protocol functional specification, this port is only supported by a Hybrid switch.
FLOOD An egress-only port, this logical port uses the replication engine of the network element to send the packet out all standard (nonreserved) ports.
FLOOD differs from ALL (another reserved port) in that ALL includes the ingress port. FLOOD leverages the element packet replication engine

## Slide 13
CONTROLLER Allows the flow rule to forward packets (over the control channel) from data path to the controller (and the reverse). This enables PACKET_IN and PACKET_OUT behavior.
The forwarding paradigm offers two modes: proactive (pre-provisioned) and reactive (data-plane driven).
Proactive mode, the control program places forwarding en‐ tries ahead of demand.
Reactive Mode, If the flow does not match an existing entry, the operator has two (global) options—to drop the flow or to use the PACKET_IN option to make a decision to create a flow entry that accommodates the packet (with either a positive/ forward or negative/disposition).

## Slide 14: Replication
Replication in Software-Defined Networking (SDN) refers to the mechanisms and strategies used to duplicate data or control information to ensure reliability, fault tolerance, and load balancing in an SDN environment.
OpenFlow provides several mechanisms for packet replication.
Group tables are a powerful feature in OpenFlow that enable more complex action behaviors, including packet replication.
Group tables allow the grouping of ports into an output port set to support multicasting, multipath, indirection, and fast-failover.
Each group table is essentially a list of action buckets (where ostensibly one of the actions is output, and an egress port is indicated). There are four group table types, but only two are required.
All - Used for multicast all action buckets in the list have to be executed.
Indirect - Used to simulate the next hop convergence behavior in IP forwarding for faster convergence.
Action lists in the Apply action (the Apply action was a singleton in OpenFlow version 1.0) allow successive replications by creating using a list of output/port actions.

## Slide 15: FAWG (Forwarding Abstraction Workgroup)
a communication protocol that enables the control of network devices, such as switches and routers, by external software controllers.
FAWG focuses specifically on defining and filtering the abstraction of forwarding behaviors (such as packet matching, modification, and forwarding) within the OpenFlow framework.
Aim is to standardizing the interfaces between the control plane and the forwarding plane in Software-Defined Networking (SDN).
The model for an OpenFlow switch works well on a software-based switch or a hardware forwarding entity that conforms to some simplifying assumptions (e.g., large, wide, deep, and multi-entrant memories like a TCAM).

## Slide 16
A separate workgroup, FAWG, is attempting a first-generation, negotiated switch model through table type patterns (TTPs).
FAWG has developed a process of building, identifying (uniquely), and sharing TTPs.
The negotiation algorithm (built on a Yang model) and messaging to establish an agreed TTP between controller and switch is also being developed (a potential addition to of-config version 1.4).
A TTP model is a predefined switch behavior model (e.g., HVPLS_over_TE forwarder and L2+L3+ACL) represented by certain table profiles (match/mask and action) and table interconnections (a logical pipeline that embodies a personality).
These profiles may differ based on the element’s role in the service flow (e.g., for the HVPLS forwarder, whether the element is head-end, mid-point, or egress).

## Slide 17
Early model contributions suggest further extensions may be required to achieve TTP in OpenFlow version 1.3.x.
If FAWG is successful, it may be possible for applications above the controller to be aware of element capabilities, at least from a behavior profile perspective.
Table Type Patterns (TTPs):
Templates that describe the structure and capabilities of the forwarding tables within a network device.
TTPs define how forwarding tables are organized and how they can be programmed by the control plane.