## Slide 1: Switch Considerations, Creating Network Virtualization Tunnels, Offloading Flows in the Data Center, Access Control for the Campus, Traffic Engineering for Service Providers, SDN Use Cases- Use Cases for Bandwidth Scheduling
Ref. 1, Ch.10.10, 10.11, 10.12, 10.13, 10.14
Ref. 2, Ch.10 (Page. 281 to Page 294)
SESSION 8
UNIT-IV

## Slide 2: Switch Considerations
Hardware switches vary in their flow capacity, feature limitations, and performance, and these should be considerations in creating an SDN application. The major issue regarding flow capacity is how many flow entries the hardware ASIC is capable of holding. Some switches support fewer than 1,000 flow entries, whereas other, such as the NEC PF5240 [8], support greater than 150,000.
Hardware implementations often have feature limitations because, when the OpenFlow specification is mapped to the capabilities of the hardware, generally some features cannot be supported. For example, some ASICs are not able to perform NORMAL forwarding on the same packet that has had its header modified in some way.
Some hardware switches will implement some functions in hardware and others in software. It is wise to understand this distinction so that an application does not cause unexpected performance degradation by unknowingly manipulating flows such that the switch processes packets in software.
In general, software implementations of OpenFlow are able to implement the full set of functionality defined by the OpenFlow specification and can implement flow tables in standard computer memory.
Thus, the feature limitations and table size issues we have described above are not a major concern for application developers. However, performance will still be a consideration, since implementations in hardware will generally be faster

## Slide 3: Creating Network Virtualization Tunnels
Figure shows a possible software application design for creating and managing overlay tunnels.
We see in the figure the switch, device, and message listeners commonly associated with reactive applications.
This reactive application runs on the controller and listens for IP packets destined for new IP destination addresses for which no flow entries exist. When the message listener receives such an unmatched packet, the application’s tunnel manager is consulted to determine which endpoint switch is responsible for this destination host’s IP address.
The information about the hosts and their tunnel endpoints is maintained by the application in the associated host and tunnel databases. The information itself can be gathered either outside the domain of OpenFlow or it could be generated by observing source IP addresses at every switch. Whichever way this is done, the information needs to be available to the application.

## Slide 4
When a request is processed, the tunnel information is retrieved from the database and, if the tunnel does not already exist, it will be created. Note that there may be other hosts communicating between these same two switches acting as tunnel endpoints, so there may be a tunnel already in existence.
The tunnel creation is performed on the OpenFlow device and a mapping is established between that tunnel and a virtual port, which is how tunnels are represented in flow entries. These methods are often proprietary and specific to a particular vendor.
Once the tunnel is either created or identified, the tunnel application can set up flows on the local switch to direct traffic heading toward that destination IP address into the appropriate tunnel. Once the virtual port exists, it is straightforward to create flow entries such as those shown in the figure, where we see the tunneled packets directed to virtual ports TUNNEL-23 and TUNNEL-12. The complementary flow will need to be set on the switch hosting the remote tunnel endpoint as well.

## Slide 5: Offloading Flows in the Data Center
Figure depicts a high-level design of an offload application. This proactive application uses RESTful APIs to communicate with the controller. The general overview of the operation of such an application is as follows:
There is a flow monitor that monitors flows and detects the beginning of an elephant flow.
Once an elephant flow is detected, the flow monitor sends a notification message (possibly using the application’s own REST API) to communicate details about the flow. This includes identifying the two endpoint ToR switches where the flow begins and ends as well as the IP addresses of the starting (1.1.1.5) and ending (2.2.2.10) hosts.
The offload application has been previously configured with the knowledge of which ports on the ToR switches connect to the offload switch.
Armed with this topology information, the offload application is able to set flows appropriately on the ToR switches and the offload switch.

## Slide 6
A new flow rule is added in this ToR switch. This is the flow shown in bold in the figure. It is important that this be a high-priority flow and match exactly on the source and destination host addresses. The next lower-priority flow entry matches on the network address 2.2.2.0/24, but, since that is a lower-priority entry, packets belonging to the elephant flow will match the higher-priority entry first, and those packets will be directed out port six to the optical offload switch. Note that traffic other than the elephant flow will match the lower-priority entries and will be transmitted via the normal port.
On the optical offload switch, flow rules are programmed that connect the two ports that will be used to forward this elephant flow between the switches involved. For the sake of simplicity, we will assume that an elephant flow is unidirectional. If there is bulk traffic in both directions, the steps we describe here can be duplicated to instantiate a separate OTN flow in each direction.
Once the elephant flow ceases, the offload application will be informed by the flow monitor and the special flows will be removed.

## Slide 7: Access Control for the Campus
SDN network access control (NAC) application for the campus. Figure shows a high-level design of a campus NAC application.
It should be apparent from the diagram that this application is a reactive application because it needs to be notified of unauthenticated users attaching to the network.
The initial state of the switch is to have flows that allow ARP and DNS but that forward DHCP requests and responses to the controller.
The DHCP responses will be used to build a database of MAC and IP addresses for the devices attaching to the network.

## Slide 8
When the DHCP response is observed, if this is a new user, the NAC application adds the user to the database and the user’s state is unauthenticated. The application then programs a flow entry in the switch based on the user’s MAC address.
This flow in the non-underlined italics text in Figure is programmed to forward the user’s HTTP requests to the controller. Thus, when a user opens a browser, in typical captive portal behavior, the application will cause the HTTP request to be forwarded to the captive portal web server where user authentication takes place.
Normal captive portal behavior is to force an HTTP redirect, which sends the user’s browser to the desired captive portal registration, authentication, or guest login page. The controller will have programmed the switch with flows that will shunt HTTP traffic to the captive portal. No other traffic type needs to be forwarded, since the authentication takes place via the user’s web browser.
Thus the user engages in an authentication exchange with the captive portal. This could entail payment, registration, or some related mechanism. When complete, the captive portal informs the NAC application that the user is authenticated. Note that the registration server uses the application’s RESTful APIs to notify the NAC application of changes in the user’s status.

## Slide 9: Traffic Engineering for Service Providers
Figure shows a simplified design for a proactive traffic engineering application that takes traffic monitoring information into account. As shown in the figure, the flow rules in the router(s) are very simple.
Likewise, the design of the application is simple. The complexity resides inside the path computation manager component doing the path calculations and optimizing traffic over the available links.

## Slide 10: Traffic engineering reactive application design.
This problem can also be addressed using reactive application design. Figure reveals a high-level design of such an approach. The key difference between this design and the proactive one lies in the flow tables on the routers, which feature a final flow entry that forwards unmatched packets to the controller.
In this solution, initially there are no flows on the switch except for the CONTROLLER flow.
routers are not pre-configured with any specific flows other than to forward unmatched packets to the controller, as is typical for a reactive application. When these packets are received at the controller, the application’s listener passes them to the path control manager.
The path control manager then calculates the best path to the destination, given the current traffic loads. Thus the flows are established in an on-demand manner. When traffic to that destination eventually stops, the flow is removed.
The flow could be removed implicitly by aging out, or an external traffic-monitoring function could explicitly inform the application that the flow has stopped and then the flow could be deleted by the application.