## Slide 1
18ECC301T – Wireless Communications
Unit IV –Improvement on Link Performance
Week 1 : Introduction to diversity, equalization and capacity, Space diversity, Scanning diversity, Maximal ratio combiner, Equal gain diversity,
Week 2: Rake Receiver, Capacity in AWGN, Capacity of flat fading channels, Equalizer and its mode, Adaptive equalizer block diagram
Week 3: Types of Equalizers - elementary level only, Introduction to MIMO antennas, Case study: Recent trends in Diversity and MIMO antenna
References :
Rappaport T.S, “Wireless Communications: Principles and Practice”, Pearson education, 2nd edition, 2009.
Andrea Goldsmith, “Wireless Communications”, Cambridge University Press, Aug 2005

## Slide 2
WEEK-2
Types of Equalizers - elementary level only, Introduction to MIMO antennas, Case study: Recent trends in Diversity and MIMO antenna

## Slide 3
types
structures
adaptive
algorithm
equalizer
linear
non-linear
transversal
lattice
DFE
ML symbol
detector
MLSE
transveral
lattice
Transversal
Channel
Estimator
0-forcing,
LMS, RLS
Fast RLS,
Sq. Root RLS
Gradient RLS
LMS, RLS,
Fast RLS
Sq. Roor RLS
Gradient RLS
LMS, RLS,
Fast RLS
Sq. Roor RLS
Types of Equalizers

## Slide 4: MIMO Wireless Communications
Single Input Single Output (SISO)
Tx
Rx
Ant 1 Ant 1
Fig. 1 SISO system
What will happen if Tx and Rx employs multiple antennas?

## Slide 5: MIMO Wireless Communications
Multiple Input Multiple Output (MIMO)?
Ant 1
Ant 1
Ant 2
Tx
Rx
Ant 2
Ant NT
Ant NR
.
.
.
.
.
.
Fig. 2 NT × NR MIMO system
channel

## Slide 6: MIMO Wireless Communications
What are advantages of MIMO?
Capacity (C) for Single Input Single Output (SISO) system
C  BW log2 1 SNR
Data rate increase when
  Bandwidth (BW) and
  Signal to noise (SNR) power increase
Inherent problems:
BW is precious, almost and always fixed for different applications

## Slide 7: MIMO Wireless Communications
Signal power increase
  battery lifetime decrease
  creates higher interference needs expensive RF amplifier
In MIMO, spectral efficiency increase
  Without increasing BW and
  Signal power

## Slide 8: MIMO Wireless Communications
But, how?
Basically two gains for MIMO systems:
– (i) MUX/rate gain
– Capacity behavior
RSNR
r 
lim
SNR   log 2 SNR
R  r log2 SNR

## Slide 9: MIMO Wireless Communications
For instance
How much is the achievable rate gain?
Ant 1
Ant 1
Ant 2
Tx
Rx
Ant 2
Ant 3
Ant 3
R  3log2 SNR
Fig. 3 Achievable rate gain with 3 × 3 MIMO system
P/S
S/P
r=3

## Slide 10: MIMO Wireless Communications
(ii) Diversity gain
Error probability behavior (minimize it) Pe SNR  SNR
d
Slope of symbol error rate/ bit error rate (SER/BER curve increases)
Behavior of error probability w.r.t. average transmit power in log-log scale
for asymptotically high power
log2 Pe SNR
log2 SNR
d  
lim
SNR  

## Slide 11: MIMO Wireless Communications
How much is diversity gain?
Ant 1
Ant 1
Ant 2
Pe SNR  SNR
9
For SISO (Rayleigh fading case), d=1,
Tx
Rx
Ant 2
Ant 3
Ant 3
Fig. 4 Diversity gain of 3 × 3 MIMO system
d=9
Pe SNR  SNR
1

## Slide 12: MIMO Wireless Communications
How much is rate and diversity gain?
Ant 1
Ant 1
Tx
Rx
r=1
Ant 2
Ant 2
Ant 3
Ant 3
Fig. 5 Rate and diversity gain of 3 × 3 MIMO system (Case I)
d=4
R  log2 SNR
Pe SNR  SNR
4

## Slide 13: MIMO Wireless Communications
How much is rate and diversity gain?
Ant 1
Ant 1
Tx
Rx
r=2
Ant 2
Ant 2
Ant 3
Ant 3
Fig. 6 Rate and diversity gain of 3 × 3 MIMO system (Case II)
d=1
R  2 log2 SNR
Pe SNR  SNR
1

## Slide 14: MIMO Wireless Communications
Need for a proper design for MIMO systems
As r decrease, d increase
As r increase, d decrease
Diversity-multiplexing trade-off [1]
 NT  r N R  r ,0  r  minNT , NR 
dopt

## Slide 15: MIMO Wireless Communications
Narrowband MIMO System Model
Ant 1
Ant 1
h12
h11
x1
y1
Tx
Rx
Ant 2
Ant 2
Fig. 7 Narrowband MIMO system model for 2 × 2 MIMO system
h21
h22
x2
y2

## Slide 16: Introduction to MIMO systems and antennas
The use of multiple antennas at the transmitter and receiver in wireless systems, popularly known as MIMO (multiple-input multiple-output) technology.
Communication in wireless channels is impaired predominantly by multi-path fading.
Communication in wireless channels is impaired predominantly by multi-path fading.
Receiver
•
•
•
Transmitter
•
•
•

## Slide 17: Introduction to MIMO systems and antennas
Multi-path is the arrival of the transmitted signal at an intended receiver through differing angles and/or differing time delays and/or differing frequency (i.e., Doppler) shifts
Due to the scattering of electromagnetic waves in the environment.
Consequently, the received signal power fluctuates in space (due to angle spread) and/or frequency (dueto delay spread) and/or time (due to Doppler spread) through the random superposition of the impinging multi-path components.
MIMO System exploits spatial dimension in addition to the time and frequency dimensions.

## Slide 18: Benefits of MIMO Technology
The benefits of MIMO technology that help achieve such significant performance gains are
array gain, spatial diversity gain, spatial multiplexing gain and interference reduction
Array gain is the increase in receive SNR that results from a coherent combining effect of the wireless signals at a receiver.
The coherent combining may be realized through spatial processing at the receive antenna array and/or spatial pre-processing at the transmit antenna array.
Array gain improves resistance to noise, thereby improving the coverage and the range of a wireless network.
signal level at a receiver in a wireless system fluctuates or fades.
Spatial diversity gain mitigates fading and is realized by providing the receiver with multiple (ideally independent) copies of the transmitted signal in space, frequency or time.

## Slide 19: Benefits of MIMO Technology
Number of copies is often referred to as the diversity order, the probability that at least one of the copies is not experiencing a deep fade increases, thereby improving the quality and reliability of reception.
A MIMO channel with M transmit antennas and N receive antennas potentially offers MN independently fading links, and hence a spatial diversity order of MN
MIMO systems offer a linear increase in data rate through spatial multiplexing, i.e., transmitting multiple, independent data streams within the bandwidth of operation.
In general, the number of data streams that can be reliably supported by a MIMO channel equals the minimum of the number of transmit antennas and the number of receive antennas, i.e., min(M, N).
The spatial multiplexing gain increases the capacity of a wireless network.
Interference in wireless networks results from multiple users sharing time and frequency resources.
Interference may be mitigated in MIMO systems by exploiting the spatial dimension to increase the separation between users.

## Slide 20: Basic TX/RX Block diagram

## Slide 21: MIMO channel and Signal model
For a system with N transmit antennas and M receive antennas, assuming frequency-flat fading over the bandwidth of interest, the MIMO channel at a given time instant may be represented as an M x N matrix.
where Hm,n is the (single-input single-output) channel gain between the mth receive and nth transmit antenna pair.
The nth column of H is often referred to as the spatial signature of the nth transmit antenna across the receive antenna array.
The relative geometry of the N spatial signatures determines the distinguishability of the signals launched from the transmit antennas at a receiver.
This is particularly important when independent data streams are launched from the transmit antennas, as is done in the case of spatial multiplexing

## Slide 22: Outage capacity and multiplexing gain
The capacity of a communication channel is the maximum, asymptotic (in block length) error-free transmission rate that can be achieved. The capacity of a MIMO channel is a complicated function of the channel conditions and transmit/receive processsing constraints.
The p percentage outage capacity at SNR ρ, Cout,p(ρ), is defined as the transmission rate that can be supported by (100−p)% of the fading realizations of the channel.
Hence at SNR , if a frame is transmitted with rate Cout,p (ρ), the probability that the frame will be decoded correctly is (100−p)%.

## Slide 23: Multiplexing gain
The maximum multiplexing gain rmax that can be achieved over a MIMO channel is given by the asymptotic (in SNR) slope of the outage capacity (for fixed FER) plotted as a function of the SNR on a linear–log scale, i.e.,

## Slide 24: Diversity gain
The maximum diversity gain dmax that can be achieved over a MIMO channel is given by the negative of the asymptotic (in SNR) slope of FER for a fixed transmission rate, plotted as a function of SNR on a log–log scale, i.e.,

## Slide 25: Case study: Recent trends in Diversity and MIMO antenna
Massive MIMO for 5G: From Theory to Practice

## Slide 26: How to realize 5G?
Key requirement of 5G: 1000-fold capacity
How to realize this goal from Shannon capacity?
Three technical directions for 5G
C = D * W * M * log (1+SINR)
No. of APs Bandwidth
No. of antennas
Interference mitigation
26

## Slide 27: What is massive MIMO?
Use hundreds of BS antennas to simultaneously serve multiple users
Conventional MIMO
M:2~8, K:1~4 (LTE-A)
Conventional MIMO
M:2~8, K:1~4 (LTE-A)
Massive MIMO
M: ~100~1000, K: 16~64
Massive MIMO
M: ~100~1000, K: 16~64
T. L. Marzetta, “Non-cooperative Cellular Wireless with Unlimited Numbers of Base Station Antennas,” IEEE Transactions on Wireless Communications, vol. 9, no. 11, pp. 3590-3599, Nov. 2010. (2013 IEEE Marconi prize)
27

## Slide 28: Why Massive MIMO ?
Spatial multiplexing
  Rate: min Nr, Nt log 1 + SNR
Reliability
  pe ∼ SNR–NrNt
Array gain (beamforming)
  Several antennas can be used to transmit signals
No. of antennas | Error Probability (pe) | Capacity (C), bps/Hz
Nt = 1, Nr = 1 (SISO) | pe ∼ SNR–1 | C = log 1+ SNR
Nt = 1, Nr > 1 (SIMO) | pe ∼ SNR–Nr | C = Nrlog 1+ SNR
Nt > 1, Nr > 1 (MIMO) | pe ∼ SNR–NtNr | C = min Nt, Nr log 1 + SNR
 | NtNr: Diversity Gain | min Nr, Nt : Multplexing Gain
28
Massive Nt, Nr: significantly increased spectral efficiency

## Slide 29: Ideal Channels
Massive MIMO has much larger ordered singular values than conventional MIMO
29
F. Rusek, D. Persson, B. Lau, E. Larsson, T. Marzetta, O. Edfors, and F. Tufvesson, “Scaling up MIMO: Opportunities and challenges with very large arrays,” IEEE Signal Processing Magazine, vol. 30, no. 1, pp. 40-60, Jan 2013.

## Slide 30: Recent Advances of Massive MIMO
Feb. 2012, Rice university & Bell labs, Argos, 64 antennas, 15 users, 85 bit/s/Hz, 1/64 power consumption
Sep. 2013, Rice university & Bell labs, ArgosV2, 96 antennas, 32 users
July 2013, Linköping & Lund University, 128
antennas, 36 users
30

## Slide 31: World’s First Massive MIMO Prototype
31
Samsung, 2014

## Slide 32: Advantages and challenges
32
Advantages
  Improve the spectrum efficiency by orders of magnitude
  Improve the energy efficiency by orders of magnitude
Challenges
  Theoretical analysis with practical constraints
  Reduce the power consumption of RF chains
  Pilot contamination in the uplink
  Efficient pilot design and channel estimation algorithm
  Efficient channel feedback mechanism
  Low-complexity near-optimal signal detection algorithm

## Slide 33: Millimeter-Wave Massive MIMO
Advantages
  Larger bandwidth: 50MHz → 1GHz
    More users and more traffic
  Larger antenna array: 1~8 → 64~256
    Larger antenna gain to compensate serious path loss
    More data streams to improve spectral efficiency
mmWave
High frequencies
Short wavelength
Serious path-loss
Spectrum expansion
Large antenna array
Small cell
1000x data rates increase!
Xinyu Gao, Linglong Dai, Shuangfeng Han, Chih-Lin I, and Robert Heath, “Energy-Efficient Hybrid Analog and Digital Precoding for mmWave MIMO Systems with Large Antenna Arrays”, to appear in IEEE Journal on Selected Areas in Communications, available at: http://arxiv.org/abs/1507.04592

## Slide 34: Challenges of mmWave massive MIMO
Challenges
  Traditional MIMO: one dedicated RF chain for one antenna
    Enormous number of RF chains due to large antenna array
    High complexity in signal processing
    Unaffordable energy consumption (250 mW per RF chain)
      64 antennas → 64 RF chains → 16 W !
How to reduce the required
number of RF chains?
How to reduce the required number of RF chains?

## Slide 35: Category 1: Hybrid beamforming
Basic idea [Ayach’14,Gao’15]
  Decompose fully digital beamformer of large size:
    Digital beamformer with small size (realized by RF chains)
    Analog beamformer with large size (realized by phase shifters)
Performance
  Reduce RF chains by signal processing
  Not obvious performance loss
  Require complicated design
  High computational complexity
[Ayach’14] O. El Ayach, et al., “Spatially sparse precoding in millimeter wave MIMO systems,” IEEE Trans. Wireless Commun., 2014.
[Gao’15] X. Gao, et al., “Energy-efficient hybrid analog and digital precoding for mmwave MIMO systems with large antenna arrays,”
IEEE J. Sel. Areas Commun., 2015.





## Slide 36: Category 2: Beamspace MIMO
Basic idea [Brady’14]
  Transform spatial channel into beamspace channel (realized by lens)
    Limited scatters → beamspace channel is approximately sparse
  Select beams to reduce dimension (realized by switching network)
  Digital beamformer with small size (realized by RF chains)
Performance
  Reduce RF chains by discrete lens array (DLA)
  Classical beamformers can be directly employed
  Low computational complexity
[Brady’14] J. Brady, et al., “Beamspace MIMO for millimeterwave communications: System architecture, modeling, analysis, and measurements,” IEEE Trans. Ant. and Propag., vol. 61, no. 7, pp. 3814–3827, Jul. 2013.
A different but promising thought to reduce RF chains
A different but promising thought to reduce RF chains

## Slide 37: Massive MIMO with Spatial Modulation
Spatial Modulation (SM)
  Exploit antenna selection pattern to transmit extra data
  Energy efficient but spectrum inefficient
Massive SM-MIMO
  Exploit more antennas to increase the spectrum efficiency
  Key challenges: signal detection and channel estimation
Zhen Gao, Linglong Dai, Zhaocheng Wang, Sheng Chen, and Lajos Hanzo, “Compressive Sensing Based Multi-User Detector for Large-Scale SM-MIMO Uplink,” to appear in IEEE Transactions on Vehicular Technology.

## Slide 38: Extension of Massive MIMO
Massive MIMO for THz
Massive MIMO and NOMA
Massive MIMO for UDN
Massive MIMO for Energy Harvesting
Massive MIMO for Wireless Power Transfer
Linglong Dai, Bichai Wang, Yifei Yuan, Shuangfeng Han, Chih-Lin I, and Zhaocheng Wang, “Non-Orthogonal Multiple Access for 5G: Solutions, Challenges, Opportunities, and Future Research Trends,” IEEE Communications Magazine, vol. 53, no. 9, pp. 74-81, Sep. 2015.

## Slide 39: Summary on the case study
Massive MIMO is very promising technology for 5G wireless communications
Theoretically, massive MIMO can increase the spectrum and energy efficiency by orders of magnitude
Several practical solutions to address challenging problems to realize massive MIMO
  Performance analysis with practical constraints
  Pilot decontamination based on graph coloring
  Efficient pilot design and channel estimation based on CS
  Low-complexity multi-user detection for uplink massive SM-MIMO
  Energy-efficient SIC-based hybrid precoding
  Beamspace massive MIMO
Future research directions
  mmWave massive MIMO, massive SM-MIMO, beamspace massive MIMO
  Massive MIMO for NOMA, UDN, THz, energy harvesting, wireless power transfer…