## Slide 1: 18ECE220T – Unit 4 S7, S8 - Spectrum Management
Dr. Diwakar R. Marur
Mr. P. Prabhu

## Slide 2: SPECTRUM MANAGEMENT CHALLENGES
CR networks impose unique challenges due to their coexistence with primary networks as well as diverse QoS requirements.
Critical Design Challenges
  Interference avoidance: CR networks should avoid interference with primary networks.
  QoS awareness: To decide on an appropriate spectrum band, CR networks should support QoS-aware communication, considering the dynamic and heterogeneous spectrum environment.
  Seamless communication: CR networks should provide seamless communication regardless of the appearance of primary users.
To address these challenges, we provide a directory for different functionalities required for spectrum management in CR networks.

## Slide 3: Four Steps - Spectrum Management Process
Spectrum sensing: A CR user can allocate only an unused portion of the spectrum. Therefore, a CR user should monitor the available spectrum bands, capture their information, and then detect spectrum holes.
Spectrum decision: Based on the spectrum availability, CR users can allocate a channel. This allocation not only depends on spectrum availability, but is also determined based on internal (and possibly external) policies.
Spectrum sharing: Because there may be multiple CR users trying to access the spectrum, CR network access should be coordinated to prevent multiple users colliding in overlapping portions of the spectrum.
Spectrum mobility: CR users are regarded as visitors to the spectrum. Hence, if the specific portion of the spectrum in use is required by a primary user, the communication must be continued in another vacant portion of the spectrum.
.

## Slide 4: Spectrum management framework for CR
It is evident from the significant number of interactions that the spectrum management functions require a cross-layer design approach

## Slide 5: 1. SPECTRUM SENSING
A CR should be aware of and sensitive to the changes in its surroundings.
Spectrum sensing is an important need for the realization of CR networks.
Spectrum sensing helps to spectrum holes without causing interference to the primary network. This can be accomplished through a real-time wideband sensing capability to detect weak primary signals in a wide spectrum range.
Generally, spectrum sensing techniques can be classified into three groups:
  Primary transmitter detection
  Primary receiver detection
  Interference temperature management

## Slide 6: 1.1 PRIMARY TRANSMITTER DETECTION
Transmitter detection is based on the detection of a weak signal from a primary transmitter through the local observations of CR users.
Following three schemes are generally used for transmitter detection:
  Matched filter detection,
  Energy detection, and
  Feature detection
Lack of interactions between primary users and CR users, transmitter detection techniques rely only on weak signals from the primary transmitters. Hence, transmitter detection techniques alone cannot avoid interference to primary receivers because of the lack of primary receiver information as depicted in Fig. 4a.

## Slide 7: 1.1 PRIMARY TRANSMITTER DETECTION (2)
Transmitter detection models cannot prevent the hidden terminal problem. A CR user (transmitter) can have a good line of sight to a CR receiver but may not be able to detect the primary transmitter due to shadowing, as shown in Fig. 4b.
For more accurate primary transmitter detection go for cooperative detection.
Advantages
  Cooperative detection is theoretically more accurate because the uncertainty in a single user’s detection can be minimized through collaboration.
  Moreover, multipath fading and shadowing effects can be mitigated so that the detection
Disadvantage:
  Causes adverse effects on resource constrained networks due to the overhead traffic required for cooperation.

## Slide 8: Transmitter detection problem
Figure 4a) receiver uncertainty; 4b) shadowing uncertainty.

## Slide 9: 1.2 PRIMARY RECEIVER DETECTION
Although cooperative detection reduces the probability of interference, the most efficient way to detect spectrum holes is to detect the primary users that are receiving data within the communication range of a CR user.
Usually, the Local Oscillator (LO) leakage power emitted by the RF front-end of the primary receiver is exploited.
However, because the LO leakage signal is typically weak, implementation of a reliable detector is not trivial.
Currently, this method is only feasible in the detection of TV receivers.

## Slide 10: 1.3 INTERFERENCE TEMPERATURE MANAGEMENT
Traditionally, interference can be controlled at the transmitter through the radiated power and location of individual transmitters. However, interference actually takes place at the receivers, as shown in Fig. 4a.
New model for measuring interference, referred to as interference temperature, is introduced by the Federal Communications Commission (FCC).
This model limits the interference at the receiver through an interference temperature limit, which is the amount of new interference the receiver could tolerate.
As long as CR users do not exceed this limit, they can use the spectrum band. Although this model is the best fit for the objective of spectrum sensing, the difficulty of this model lies in accurately determining the interference temperature limit.

## Slide 11: 2. Spectrum decision
SPECTRUM DECISION: CR networks require the capability to decide which is the best spectrum band among the available bands according to the QoS requirements of the applications.
Spectrum decision is closely related to the channel characteristics and operations of primary users. Furthermore, spectrum decision is affected by the activities of other CR users in the network.
Step ONE: Each spectrum band is characterized, based on not only local observations of CR users but also statistical information of primary networks.
Step TWO: Based on this characterization, the most appropriate spectrum band can be chosen.

## Slide 12: 2.1 CHANNEL CHARACTERISTICS
Spectrum holes characteristics vary over time, each spectrum hole should be characterized considering both the time-varying radio environment and spectrum parameters, such as operating frequency and bandwidth.
Essential parameters for a particular spectrum band as follows:
  Interference
  Path loss
  Wireless link errors
  Link layer delay

## Slide 13: 2.2 DECISION PROCEDURE
After the available spectrum bands are characterized, the most appropriate spectrum band should be selected, considering the QoS requirements and spectrum characteristics. Accordingly, the transmission mode and bandwidth for the transmission can be reconfigured.
To describe the dynamic nature of CR networks, a new metric — primary user activity — is proposed.
It is defined as the probability of a primary user appearance during CR user transmission.
  Because there is no guarantee that a spectrum band will be available during the entire communication of a CR user, it is important to consider how often the primary user appears on the spectrum band.
Due to the operation of primary networks, CR users cannot obtain a reliable communication channel for a long time period.
Sometimes, CR users may not detect any single spectrum band to meet the user’s requirements

## Slide 14: 3. SPECTRUM SHARING
The shared nature of the wireless channel requires the coordination of transmission attempts between CR users.
Spectrum sharing should include much of the functionality of a MAC protocol. Moreover, the unique characteristics of CRs, such as the coexistence of CR users with licensed users and the wide range of available spectrum, incur substantially different challenges for spectrum sharing in CR networks.
The existing work in spectrum sharing aims to address these challenges and can be classified by four aspects:
  The architecture,
  Spectrum allocation behavior,
  Spectrum access technique,
  Scope.

## Slide 15: Classification Spectrum Sharing Techniques
TYPE I
  Centralized spectrum sharing
  Distributed spectrum sharing
TYPE II
  Cooperative spectrum sharing
  Non-cooperative spectrum sharing
TYPE III
  Overlay spectrum sharing
  Underlay spectrum sharing
TYPE IV
  Intranetwork spectrum sharing
  Internetwork spectrum sharing

## Slide 16: 4. SPECTRUM MANAGEMENT
After a CR captures the best available spectrum, primary user activity on the selected spectrum may necessitate that the user change its operating spectrum band(s), which is referred to as spectrum mobility.
Spectrum mobility gives rise to a new type of handoff in CR networks, spectrum handoff.
Protocols for different layers of the network stack must adapt to the channel parameters of the operating frequency.
Protocols should be transparent to spectrum handoff and the associated latency.
Each time a CR user changes its frequency of operation, the network protocols may require modifications to the operation parameters.

## Slide 17: 4. SPECTRUM MANAGEMENT (2)
The purpose of the spectrum mobility management in CR networks is to ensure smooth and fast transition leading to minimum performance degradation during a spectrum handoff.
Information about the duration of a spectrum handoff is an important information. It is provided by the sensing algorithm.
After the latency information is available, the ongoing communications can be preserved with only minimum performance degradation.
The intrinsic characteristics of a CR network give rise to two novel concepts:
  Spectrum mobility
  Spectrum handoff.