## Slide 1: WHAT IS VSAT
Stands for “Very Small Aperture Terminal” and refers to receive / transmit terminals installed at dispersed sites connecting to a central hub via satellite using small diameter antenna dishes (0.6 to 3.8meter) @ C and KU Band Frequencies
Uses
Interactive computer transactions
Internet
Video Teleconferencing
Bank transactions, ATM
Reservation systems
Distributed remote process control and telemetry
Voice communications
Emergency services
Electronic fund transfer at Point-of-Sale
Medical
Data transfer
Sales monitoring & stock control

## Slide 2
The basic structure of a VSAT network consists of a hub station which provides a broadcast facility to all the VSATs in the network and the VSATs themselves which access the satellite in some form of multiple access mode. The hub station is operated by the service provider, and it may be shared among a number of users
Time division multiplex is the normal downlink mode of transmission from hub to the VSATs, and the transmission can be broadcast for reception by all the VSATs in a network, or address coding can be used to direct messages to selected VSATs.
The most popular access method is FDMA, which allows the use of comparatively low-power VSAT terminals.

## Slide 3
TDMA also can be used but is not efficient for low-density uplink traffic from the VSAT.
The traffic in a VSAT network is mostly data transfer of a bursty nature, examples being inventory control, credit verification, and reservation requests occurring at random and possibly infrequent intervals, so allocation of time slots in the normal TDMA mode can lead to low channel occupancy
demand assigned multiple access (DAMA) is can be used with FDMA as well as TDMA, but the disadvantage of the method is that a reserve channel must be instituted through which the VSATs can make requests for channel allocation.

## Slide 4
The method of code-division multiple access (CDMA) using spread spectrum techniques, coupled with the Aloha protocol. The basic Aloha method is a random-access method in which packets are transmitted at random in defined time slots.
VSAT systems operate in a star configuration, which means that the connection of one VSAT to another must be made through the hub.
The VSAT system which also provides for mesh connection, where the VSATs can connect with one another through the satellite in a single hop.

## Slide 5
Advantages
Fixed area coverage- Ku band is used for operation of most VSAT systems
System performance is independent of carrier frequency.
Beamwidth and λ/D ration are constant
Antenna gain is constant
EIRP remains constant
Drawbacks
High initial costs
NO direct VSAT to VSAT link I are available

## Slide 6: Global Positioning Satellite System ( GPS )
In the GPS system, a constellation of 24 satellites circles the earth in near-circular inclined orbits.
By receiving signals from at least four of these satellites, the receiver position (latitude, longitude, and altitude) can be determined accurately.
The only quantity the receiver has to be able to measure is time, from which propagation delay, and hence the range to each satellite, can be determined.
Knowing the range to three of the satellites and their positions, it is possible to compute the position of the observer (user).
The geocentric-equatorial coordinate system is used with the GPS system, where it is called the earth-centered, earth-fixed (ECEF)
coordinate system.

## Slide 7
The GPS constellation consists of 24 satellites in six near-circular orbits, at an altitude of approximately 20,000 km .
The ascending nodes of the orbits are separated by 60°, and the inclination of each orbit is 55°

## Slide 8: Operating Modes
Precise Positioning System (PPS) - US and allied military, authorized government agencies - 22 m horizontal, 27.7 m vertical, 100 ns accuracy (95% of time). Resistant to jamming (L1/L2)
Standard Positioning System (SPS) - civilian use - 100 m horizontal, 156 m vertical, 340 ns accuracy with S/A, improved to nearly PPS values after May 1, 2000, but with no resistance to jamming

## Slide 9
Where very high accuracy is required differential GPS (DGPS) can be used. Two receivers are used, one of which is placed at an accurately known location. Thus, the reference receiver makes a measurement in the usual way, but since the coordinates for the location are known, the only unknown in the range equ , which can now be calculated.